## Slide 1: NIGHTFALLS
Computer Graphics Object modeling and Rendering project

## Slide 2: Meteors
Meteor showers take place regularly and are one of the most fascinating phenomenon

## Slide 3: OPENGL
Legacy
3
A cross-language, cross-platform API (Application Programming Interface) used for rendering both 2D and 3D graphics.
Legacy OpenGL refers to the primitive version of OpenGL, especially those previous to 3.0
Legacy OpenGL doesn’t give user access to Vertex Buffers and thus has poorer performance
Nonetheless, it has better compatibility and is still strong enough for Many projects

## Slide 4: BLENDER
A free professional grade 3D working suite that is fully fledged for industry standard Graphics
4

## Slide 5: SDL AND VISUAL STUDIO 2019 COMMUNITY
Simple DirectMedia Layer is a cross-platform development library designed to provide low level access to audio, keyboard, mouse, joystick, and graphics hardware via OpenGL and Direct3D.
It is used by video playback software, emulators, and popular games including Valve’s award winning catalog and many Humble Bundle games.
Visual Studio is an Integrated Development Environment(IDE) created by Microsoft to create GUI(Graphical User Interface), reassure, Web applications, web applications, versatile applications, cloud, and web administrations, and so forth.

## Slide 6: OpenGL 3D Working Pipeline
The 3D graphics rendering pipeline consists of the following main stages:
Vertex Processing: Process and transform individual vertices.
Rasterization: Convert each primitive (connected vertices) into a set of fragments. A fragment can be treated as a pixel in 3D spaces, which is aligned with the pixel grid, with attributes such as position, color, normal and texture.
Fragment Processing: Process individual fragments.
Output Merging: Combine the fragments of all primitives (in 3D space) into 2D color-pixel for the display.

## Slide 7: TEAM AND WORK DIVISION
Jebish Purbey
074BEX412
Modelling – House
Coding – Main file and Object loader
Manita Dahal
074BEX414
Modelling – Bench and Terrain Modelling
Coding – Camera Movement
Nimesh Rai
074BEX415
Modelling – Trees
Coding - Skybox
Paru Hang Rai
074BEX416
Modelling – Meteors
Coding – Particle system

## Slide 8: Object Loader
Loads object with just load(“filename.obj”);
Usage of vector for efficient vertices transfers, using pushback function
Loads texture and materials details from .mtl file
Usage of Texture filter for better texture mapping

## Slide 9: OBJECT Loader
Start
Declare and define all possible variables required for loading objects
Load object loaders load function with a “obj” file
Declare a buffer of maximum 255 characters
Load each line of object file in the character buffer
Check the initial characters of the buffer for the type of parameters
Send the data with the correct format in the required variable field
If the initial characters of buffer says Texture, read the texture from mtl file and load using loadtexture function
If the initial characters of buffer says change of material, read the new details from mtl file and send to attribute variables
Delete the textures once its used for prevention of memory leak
Draw the model while it’s object is being parsed
If the total file has been read then end the function and model is displayed
END

## Slide 10: SkyBox
A six sided cube with texture that gives life to the environment
Usage of array for storing texture ID for each side
Loads textures using loadtexture() function
Sometimes light sources interferes (blends) into the skybox, so it’s recommended to disable the light source before drawing the skybox

## Slide 11: SKY Box
Initialize an array to load all the six textures of skybox
Load the texture ID to the respective elements of array
Draw the quads for that textured side with help of vertex(3D) and textured coordinates
Do the same for the remaining 5 sides
Enable the lights
Start
End
Disable the lights
Starting from one side of skybox, generate the texture, and bind it

## Slide 12: Camera Movement
Uses SDL library for Keypress and mouse detection
W S A D gives movement
Mouse movement rotates the camera : camera Yaw and Camera pitch
“P” key enables/disables the camera movement

## Slide 13: CAMERA Movement
Fig: Block Diagram to show creation of Skybox in OpenGL

## Slide 14: CAMERA Movement
Fig: Block Diagram to show creation of Skybox in OpenGL

## Slide 15: PARTICLES System
Uses glBegin(GL_LINES/GL_POINTS) for drawing the particles
A particle system is a technique in game physics, motion graphics, and computer graphics that uses many minute sprites, 3D models, or other graphic objects to simulate certain kinds of "fuzzy" phenomena, which are otherwise very hard to reproduce with conventional rendering techniques.
Usually chaotic phenomena are represented by particles
Particle has Position, updated positions, velocity, gravity and acceleration due to mass

## Slide 16: PARTICLES System
Generate particle with random mass, velocity and position
Is n > max_particle
Calculate acceleration
Start
Calculate velocity
Calculate force
n=3000
n+1
A
B
Stop
Is velocity >max_velocity
Velocity=unit velocity *max_velocity ax_velocity
Calculate position
Y position= -length Z position= -length
Is position < -length
Is last particle
Draw Particles
n+1
Y position= length Z position= length
Is position < length
Load Texture
B
A

## Slide 17: LIGHTING
Legacy OpenGL only supports ambient, diffuse lights
Thus Phong Model of shading is not usable
Only Ambient and Diffuse lights are use by initializing light sources (At max 8) with positions and their colours and intensity
Light can be enabled by :glEnable(GL_LIGHTING);

## Slide 18: BLENDING AND DEPTH TESTING
Blending is enabled via: glEnable(GL_BLEND); Depth testing enabled via: glEnable(GL_DEPTH_TEST);
Depth testing is Z-buffer test, buffer size can be set beforehand
Blending is done for having proper transparency or translucency features
Depth testing is thus important for blending
glBlendFunc();

## Slide 19: ANTI-ALIASING
MultiSample Anti Aliasing removes problem of jaggy images
Aliasing occurs sometimes because of sampling, sometime because texture image is larger than pixels to map it
Multi Sample Anti Aliasing – A no of samples at the points of each edges takes, and final vertex or texture colour at that point will be the average of all the samples
Reduces jagging images but requires performance power
Sa
SDL_GL_SetAttribute(SDL_GL_MULTISAMPLEBUFFERS,1); SDL_GL_SetAttribute(SDL_GL_MULTISAMPLESAMPLES,16);
19

## Slide 20: Quote and Image Slide
“
RESULT
20

## Slide 21: Quote and Image Slide
“
RESULT
21

## Slide 22: ADVANTAGES
Compatibility will almost all Computers that can run OpenGL , almost all versions
Easier to code and thus debug
Beginners friendly
No need to write shaders for Lightings and rendering, makes the process faster and easier
22

## Slide 23: LIMITATIONS
Requires a huge processing power
Phong Illumination Model is not possible
No vertices buffers thus performance suffers
Easier to implement but doesn’t provide full customizations
23

## Slide 24: THANK YOU
Insert Image